## Slide 1
CPU LAB for Computer Organization
處理器設計與實作

## Slide 2
LAB 6
Verilog Implementation Of I-Cache

## Slide 3: 實驗目的
認識MIPS CPU的Memory Hierarchy
學習Verilog module之應用
了解I-Cache的架構與行為

## Slide 4: Levels of Memory Hierarchy
CPU
Registers
Main Memory (DRAM)
Secondary Storage (Hard Disk)
Cache
Upper Level
(Faster)
Lower Level
(larger)

## Slide 5: The Principle of Locality
Temporal Locality (Locality in Time):
If an item is referenced, it will tend to be referenced again
soon.
( Example: loop, reuse )
Spatial Locality (Locality in space):
If an item is referenced, items whose addresses are close
by tend to be referenced soon.
( Example: array access, straight line code )

## Slide 6: Introduction to Cache System
Insert between CPU and Main Memory
Implemented with fast Static Ram
Holds some of a program’s
  Data (D-Cache)
  Instructions (I-Cache)
CPU
addr.
addr.
data
data
Processor
Cache Memory
(K Bytes)
Main Memory
(G Bytes)

## Slide 7: Cache Operation
CPU sends an address to Cache
Hit : Data in Cache (no penalty)
Miss: Data not in Cache
(miss penalty)
CPU
addr.
addr.
data
data
Processor
Cache Memory
(K Bytes)
Main Memory
(G Bytes)
Cache Hit

## Slide 8: Cache Operation
CPU sends an address to Cache
Hit : Data in Cache (no penalty)
Miss: Data not in Cache
(miss penalty)
CPU
addr.
addr.
data
data
Processor
Cache Memory
(K Bytes)
Main Memory
(G Bytes)
Cache Hit

## Slide 9: Cache Operation
CPU sends an address to Cache
Hit : Data in Cache (no penalty)
Miss: Data not in Cache
(miss penalty)
CPU
addr.
addr.
data
data
Processor
Cache Memory
(K Bytes)
Main Memory
(G Bytes)
Cache Miss !

## Slide 10: Cache Operation
CPU send an address to Cache
Hit : Data in Cache (no penalty)
Miss: Data not in Cache
(miss penalty)
CPU
addr.
addr.
data
data
Processor
Cache Memory
(K Bytes)
Main Memory
(G Bytes)
Cache Miss !

## Slide 11: Cache Operation
CPU sends an address to Cache
Hit : Data in Cache (no penalty)
Miss: Data not in Cache
(miss penalty)
CPU
addr.
addr.
data
data
Processor
Cache Memory
(K Bytes)
Main Memory
(G Bytes)
Cache Miss !
Delay

## Slide 12: Cache Performance
Hit Rate: Fraction of hits in Cache
    Miss Rate = 1 – (Hit Rate)
Hit Time: Time to access Cache
Miss Penalty: Time to replace a block from lower level
Average memory-access time ( AMAT )
= Hit Time + Miss rate x Miss penalty

## Slide 13: Direct Mapped Block Placement
Main Memory
Cache
00
04
08
0c
10
14
18
1c
20
24
28
2c
30
34
38
3c
*0
*4
*8
*c
Index
0
1
2
3
Data

## Slide 14: Direct Mapped Example
Cache
The sequence of memory access: 00, 04, 08, 0c, 10
Memory Block | Hit/Miss
Index
0
4
8
c

## Slide 15: Direct Mapped Example
Cache
The sequence of memory access: 00, 04, 08, 0c, 10
Memory Block | Hit/Miss
00 | Miss
Index
0
4
8
c

## Slide 16: Direct Mapped Example
Cache
The sequence of memory access: 00, 04, 08, 0c, 10
Memory Block | Hit/Miss
00 | Miss
Mem[00]
Index
0
4
8
c
From main memory

## Slide 17: Direct Mapped Example
Cache
The sequence of memory access: 00, 04, 08, 0c, 10
Memory Block | Hit/Miss
00 | Miss
04 | Miss
Mem[00]
Index
0
4
8
c

## Slide 18: Direct Mapped Example
Cache
The sequence of memory access: 00, 04, 08, 0c, 10
Memory Block | Hit/Miss
00 | Miss
04 | Miss
Mem[00]
Mem[04]
Index
0
4
8
c
From main memory

## Slide 19: Direct Mapped Example
Cache
The sequence of memory access: 00, 04, 08, 0c, 10
Memory Block | Hit/Miss
00 | Miss
04 | Miss
08 | Miss
Mem[00]
Mem[04]
Mem[08]
Index
0
4
8
c
From main memory

## Slide 20: Direct Mapped Example
Cache
The sequence of memory access: 00, 04, 08, 0c, 10
Memory Block | Hit/Miss
00 | Miss
04 | Miss
08 | Miss
0c | Miss
Mem[00]
Mem[04]
Mem[08]
Mem[0c]
Index
0
4
8
c
From main memory

## Slide 21: Direct Mapped Example
Cache
The sequence of memory access: 00, 04, 08, 0c, 10
Memory Block | Hit/Miss
00 | Miss
04 | Miss
08 | Miss
0c | Miss
10 | Miss
Mem[10]
Mem[04]
Mem[08]
Mem[0c]
Index
0
4
8
c
From main memory

## Slide 22: Cache Line Refill Load in multi-data when cache miss

## Slide 23: Cache Line Refill : 16-byte line size
Main Memory
Cache
00
04
08
0c
10
14
18
1c
20
24
28
2c
30
34
38
3c
index
0*
1*
2*
3*
00
10
20
30
04
14
24
34
08
18
28
38
0c
1c
2c
3c

## Slide 24: Line Refill Example: 16-byte line size
Cache
The sequence of memory access: 00, 04, 08, 0c, 10
Mem Block | Hit/Miss
Index
0*
1*
2*
3*

## Slide 25: Line Refill Example: 16-byte line size
Cache
The sequence of memory access: 00, 04, 08, 0c, 10
Mem Block | Hit/Miss
00 | Miss
Index
0*
1*
2*
3*

## Slide 26: Line Refill Example: 16-byte line size
Cache
The sequence of memory access: 00, 04, 08, 0c, 10
Mem Block | Hit/Miss
00 | Miss
Mem[00]
Index
0*
1*
2*
3*
Mem[04]
Mem[08]
Mem[0c]
From main memory

## Slide 27: Line Refill Example: 16-byte line size
Cache
The sequence of memory access: 00, 04, 08, 0c, 10 (word address)
Mem Block (Word) | Hit/Miss
00 | Miss
04 | Hit
Mem[00]
Index
0*
1*
2*
3*
Mem[04]
Mem[08]
Mem[0c]

## Slide 28: Line Refill Example: 16-byte line size
Cache
The sequence of memory access: 00, 04, 08, 0c, 10
Mem Block | Hit/Miss
00 | Miss
04 | Hit
08 | Hit
Mem[00]
Index
0*
1*
2*
3*
Mem[04]
Mem[08]
Mem[0c]

## Slide 29: Line Refill Example: 16-byte line size
Cache
The sequence of memory access: 00, 04, 08, 0c, 10
Mem Block | Hit/Miss
00 | Miss
04 | Hit
08 | Hit
0c | Hit
Mem[00]
Index
0*
1*
2*
3*
Mem[04]
Mem[08]
Mem[10]

## Slide 30: Line Refill Example: 16-byte line size
Cache
The sequence of memory access: 00, 04, 08, 0c, 10
Mem Block | Hit/Miss
00 | Miss
04 | Hit
08 | Hit
0c | Hit
10 | Miss
Mem[00]
Index
0*
1*
2*
3*
Mem[04]
Mem[08]
Mem[0c]
Line size = 16 bytes

## Slide 31: Line Refill Example: 16-byte line size
Cache
The sequence of memory access: 00, 04, 08, 0c, 10
Mem Block | Hit/Miss
00 | Miss
04 | Hit
08 | Hit
0c | Hit
10 | Miss
Mem[00]
Mem[10]
Index
0*
1*
2*
3*
Mem[04]
Mem[14]
Mem[08]
Mem[18]
Mem[0c]
Mem[1c]
From main memory

## Slide 32: Address (aligned to a word for instruction)
Block Address (32-bit) |  |  | 
Tag | Index | word | 00
Index : Decide which entry of cache should be accessed
Tag : Check if the cache access is a hit or not
Word : Decide which data of entry to output
How do we decide number of bits in each part?

## Slide 33: Cache Architecture
1 | 0008… | 0x00001c0 | 0x00001c4 | 0x00001c8 | 0x00001cc
0 |  |  |  |  | 
0 |  |  |  |  | 
1 | 00c0… | 0x0024000 | 0x0024004 | 0x0024008 | 0x002400c
1 | 0000… | 0x1c00000 | 0x1x00004 | 0x1c00008 | 0x1c0000c
0 |  |  |  |  | 
0 |  |  |  |  | 
0 |  |  |  |  | 
Valid
Tag
Data
Tag
Index
Address [31:0]
000
001
010
011
100
101
110
0000 0000 0000 0000 0000 0000 0 | 100 | 10 | 00
Word
Word=0
Word=1
Word=2
Word=3
111
Index
31 7 6 4 3 2 1 0
2-bit [1:0]
2-bit [3:2]
3-bit [6:4]
32-3-2-2=25-bit [31:7]
This is a Cache with 8 entries, and each line (entry) has 4 words (data).

## Slide 34: Cache Architecture
1 | 0008… | 0x00001c0 | 0x00001c4 | 0x00001c8 | 0x00001cc
0 |  |  |  |  | 
0 |  |  |  |  | 
1 | 00c0… | 0x0024000 | 0x0024004 | 0x0024008 | 0x002400c
1 | 0000… | 0x1c00000 | 0x1x00004 | 0x1c00008 | 0x1c0000c
0 |  |  |  |  | 
0 |  |  |  |  | 
0 |  |  |  |  | 
Valid
Tag
Tag
Index
Address [31:0]
0000 0000
0000 0001
0000 0000 0000 0000 0000 | 0000 0010 | 10 | 00
Word
Word=0
Word=1
Word=2
Word=3
1111 1111
Index
31 12 11 4 3 2 1 0
2-bit [1:0]
2-bit [3:2]
8-bit [11:4]
32-8-2-2=20-bit [31:12]
If a Cache with 256 entries, and each line (entry) has 4 words (data) …
.
.
.
.
.
.

## Slide 35: Cache Architecture
1 | 0x0008 | 0x00001c0 | 0x00001c4 | 0x00001c8 | 0x00001cc
0 |  |  |  |  | 
0 |  |  |  |  | 
1 | 0x00c0 | 0x0024000 | 0x0024004 | 0x0024008 | 0x002400c
1 | 0x0000 | 0x1c00000 | 0x1x00004 | 0x1c00008 | 0x1c0000c
0 |  |  |  |  | 
0 |  |  |  |  | 
0 |  |  |  |  | 
Valid
Tag
Data
Tag
Index
Address
000
001
010
011
100
101
110
=
tag_in
tag_out
Hit = 1 ( Cache Hit )
(tag_in = tag_out) & valid_out =1
0x0000 | 100 | 10 | 00
Word
Word=00
Word=01
Word=10
Word=11
Data Output =
0x1c00008
111
Index

## Slide 36
LAB 6
Verilog Implementation Of I-Cache

## Slide 37: Tool used
實驗環境:
Modelsim (Run CPU simulator)

## Slide 38: Modelsim 安裝
1. Modelsim PE overview
http://model.com/content/modelsim-pe-simulation-and-debug
2. Modelsim PE download
http://model.com/update/modelsim-downloads

## Slide 39: Modelsim 開啟教學(1/3)
Step.1:change to our file location
打開modelsim後,在File下選擇change directory到你放\...\MIPS_cpu_test 的地方

## Slide 40: Modelsim 開啟教學(2/3)
Step.2:new project
接著new一個project(名稱自訂)

## Slide 41: Modelsim 開啟教學(3/3)
Step.3:add source code
新增完project後,會跳出一個視窗(如圖),點選Add Existing File將VHDL/Verilog source code加入到這個project中

## Slide 42: Modelsim 驗證(1/4)
點選browse，把所有的.v檔加進來

## Slide 43: Modelsim 驗證(2/4)
Compile source code
新增完 source code 之後，點選右上角的compile (實作時如果有修改程式碼，只要從compile之後重新做即可)

## Slide 44: Modelsim 驗證(3/4)
Simulate testbench
Compile 之後，點選右上角的 simulate ，選 testbench，計得要把enable optimization 取消

## Slide 45: Modelsim 驗證(4/4)
打開testbench -> u_cpu_top -> u_icache 把右邊所有 input output訊號線加到波形，就可以驗證波形是否正確

## Slide 46: 實作一
請同學以RTL code完成這顆MIPS CPU中I_Cache.v空白部分,使用ModelSim編譯完成,並且完成驗證。
Direct Mapped I-Cache :
There are 256 entries in this cache
Each entry (line) with exactly 1 word (data)

## Slide 47: Cache Architecture
1 | 0x0008 | 0x00001c24
0 |  | 
0 |  | 
1 | 0x00c0 | 0x00004c00
1 | 0x0000 | 0x00c10800
0 |  | 
0 |  | 
0 |  | 
Valid
Tag
Data
0x0000 | 4 (100) | 00
Tag
Index
Address
0
1
2
3
4
5
6
=
tag_in
tag_out
Hit = 1 ( Cache Hit )
(tag_in = tag_out) & valid_out =1
Data_Out
7
valid_out

## Slide 48: Part 1
This is a “Direct Mapped I-Cache” with 256 entries each having a 32- bit data.
ADDR [31:0] is a 32-bit signal (address) from CPU to Cache
First, you have to pass the ADDR to IADDR (send addr. to memory if cache miss)
The cache has 256 entries which means that your index should be ___ bits.
Once you know how many bits for index and tag_in, get index & tag_in from ADDR
00
index
tag_in
0
請同學根據前面的內容決定 index, tag_in 分別需要幾個 bit，並且寫出二個訊號
分別來自ADDR當中的哪一段
31

## Slide 49: Part 2
Use index to get data_out from cache memory
Use index to get tag_out from cache memory
Use index to get valid_out from cache memory
請同學根據前面的提示決定 data_out, tag_out 和 valid_out
In part2, we have to prepare data_out, tag_out and valid_out signals.
And, we need the signal “index” which we have prepared in part1 to help us.
Cache_Data
Cache_Tag
Cache_Valid
256 entries

## Slide 50: Part 3
For Cache_Hit signal, check if valid_out=1, then compare tag_in and tag_out
For IREQ signal, make sure that Enable=1 first, and check if Cache_Hit = 1 or 0
For DO signal, use output_enable to decide out data (DO_reg or 32’bz)
請同學根據前面的說明，完成Cache_Hit, IREQ, DO
Now that you have most of the signals you need, you have to decide if the cache access is a hit or not. And send the correct signals to memory and CPU.
IREQ is a signal to request data from main memory
Enable is a signal which indicates if the cache is enabled or not.
DO (Data Out) is the data from cache to CPU
output_enable is a signal indicating if the output data are ready or not
DO_reg is a register which contains the data for output

## Slide 51: Part 4
When a cache_miss happened, you have to update the data in I-Cache including Cache_Data, Cache_Tag and Cache_Valid .
Put the new data called “Data_in” into Cache_Data
Put the new tag called “tag_in” into Cache_Tag
Put the new data called “valid_in” into Cache_Valid
請同學根據前面的內容在Cache發生miss的時候更新Cache的內容
Data_in is a 32-bit data from main memory
Tag_in is the new tag which you got from part1
Valid_in is just a signal 1 which indicates that the cache line is valid.

## Slide 52: Verification
If your RTL code is correct, you will find that the cache will miss whenever the address changes

## Slide 53: 實作二
請同學以RTL code完成這顆MIPS CPU中I_Cache.v空白部分,使用ModelSim編譯完成,並且完成驗證。
This is a “Direct Mapped I-Cache”
There are 256 entries in this cache
Each entry (line) has 4 words (data).

## Slide 54: Cache Architecture
1 | 0x0008 | 0x00001c0 | 0x00001c4 | 0x00001c8 | 0x00001cc
0 |  |  |  |  | 
0 |  |  |  |  | 
1 | 0x00c0 | 0x0024000 | 0x0024004 | 0x0024008 | 0x002400c
1 | 0x0000 | 0x1c00000 | 0x1x00004 | 0x1c00008 | 0x1c0000c
0 |  |  |  |  | 
0 |  |  |  |  | 
0 |  |  |  |  | 
Valid
Tag
Data
Tag
Index
Address
000
001
010
011
100
101
110
=
tag_in
tag_out
Hit = 1 ( Cache Hit )
(tag_in = tag_out) & valid_out =1
0x0000 | 100 | 10 | 00
Word
Word=00
Word=01
Word=10
Word=11
Data Output =
0x1c00008
111
Index

## Slide 55: Part 1
This is a “Direct Mapped I-Cache” with 256 entries each has a 128 bits data.
ADDR [31:0] is a 32-bit signal (address) from CPU to Cache
First, you have to pass the ADDR to IADDR (send addr. to memory if cache miss)
The cache has 256 entries which means that your index should be ___ bits.
The cache has 4 data in each line (entry) which means that your word should be ___ bits.
Once you know how many bits index, word and tag_in need, use ADDR to complete the code
00
index
tag_in
0
請同學根據前面的內容決定 index, word, tag_in 分別需要幾個 bit，並且寫出三個訊號
分別來自ADDR當中的哪一段
31
word

## Slide 56: Part 2
We have learned how to use index and tag to check if the cache access is a hit or miss. And we also learned how to setup the signal (IREQ) for main memory, and output data (DO) for CPU.
However, there are 4 words in each line (entry). We have to decide which word to output by a 2-bit signal called “word”, before sending data to CPU.
00
index
tag_in
0
31
word
data 1
data 2
data 3
data 4
0
31
32
63
127
64
128-bit
32-bit output

## Slide 57: Part 2
Put the 32-bit data into data_out_hit_reg from data_out
Put the 32-bit data into data_out_miss_reg from data_in
data_out_hit_reg is a register which contains the data to output when cache hit
data_out is a 128-bit data which contains the data from cache
data_out_miss_reg is a register which contains the data for CPU when cache line refill completes.
data_in is a 128-bit data which contains the data from memory (assuming memory bus is 128 bits)

## Slide 58: Verification
If your RTL code is correct, you will find that the cache misses every four different address.

## Slide 59: 挑戰題
In lab 6-2, we assume the bandwidth of the bus is 128-bit, which means that we can get 4 data (128-bit) from main memory at the same time when a cache miss happened.
CACHE
Main Memory
128

## Slide 60: 挑戰題
However, the real bus can send only one data ( 32-bit ) in each access to main memory. In this situation, the cache has to access main memory four times when encounter a cache miss. (assume each line has 4 data )
CACHE
Main Memory
32

## Slide 61: 挑戰題
The followings are the files we need in this part :
1. cpu_top.v 2. I_Cache.v 3. testbench.v
I_Cache.v
testbench.v
32
memory
cpu_top.v

## Slide 62: 挑戰題
And what we are going to do is :
Change the bandwidth in “I_Cache.v”, “cpu_top.v” and “testbench.v” from 128-bit ( [127:0] ) to 32-bit ( [31:0] ).
In “I_Cache.v”, whenever a cache access is miss, sends the address to main memory, waiting for the data from main memory.
Never send the data to CPU until the line refill is complete.

## Slide 63
實驗結報
結報格式(每組一份)
  封面
  實驗內容(程式碼註解、結果截圖)
  實驗心得
繳交位置
  ftp : 140.116.164.227
  帳號/密碼 : co2012
DeadLine:下次上課前
TA Contact Information:
  助教信箱 : chen9611@gmail.com
  Rm 92617
  Office hour : (Tues)1300~1500、(Wed)1300~1400
63